DESCRIPTION

This work shall include the removal of existing signs designated on the plans or as specified by the engineer.  The sign components shall include sign panels, upright supports, bracing and structures.  Signs designated for removal shall become the property of the Monroe County Department of Transportation at no extra cost to the county.

REMOVAL OF SIGNS

Existing traffic signs requiring removal only, shall be removed from the work site in a neat and workmanlike manner to the satisfaction of the engineer.

REMOVAL OF CONCRETE SIGN FOOTINGS

All concrete sign footings shall be cut to a depth of 6” below existing ground and be replaced with suitable material as specified by the engineer.

METHOD OF MEASUREMENT

The quantity to be paid for will be the number of completely removed signs having sign areas of the following sizes:

SIZE A:		0 to 10 Square Feet

SIZE B:		11 to 20 Square Feet

SIZE C:		21 to 40 Square Feet

SIZE D:		41 to 100 Square Feet

SIZE E:		Over 100 Square Feet

BASIS OF PAYMENT

The unit price bid for removing an existing installation shall be compensation in full for the furnishing of all labor, equipment and materials necessary to complete the work to the satisfaction of the engineer.

Payment will be made under:

| Item No. | Item | Pay Unit |
| --- | --- | --- |
| C686.41 | Removal of Signs - Size A (0.0 - 10 SF) | EA |
| C686.42 | Removal of Signs - Size B (11 - 20 SF) | EA |
| C686.43 | Removal of Signs - Size C (21 - 40 SF) | EA |
| C686.44 | Removal of Signs - Size D (41 - 100 SF) | EA |
| C686.45 | Removal of Signs - Size E (over 100 SF) | EA |