DESCRIPTION

Under this item the contractor shall install a furnished controller and related equipment and a ground mounted cabinet.  The contractor shall install the said equipment as directed by the engineer.

The equipment furnished by the county will be in accordance with the Monroe County Department of Transportation Standard Specifications.

CONSTRUCTION DETAILS

The contractor shall install the furnished cabinet and controller, detectors, conflict monitor, and other related items and do the necessary wiring to complete the installation.  The cabinet shall be picked up by the contractor at the Monroe County Department of Transportation Traffic Engineering Signal Shop.

METHOD OF MEASUREMENT

The quantity to be paid for under this item will be the number of units installed in accordance with the plans and specifications.

BASIS OF PAYMENT

The unit price bid will be for each installation and shall include the cost of furnishing all labor and equipment necessary to complete the work.

Payment will be made under:

| Item No. | Item | Pay Unit |
| --- | --- | --- |
| C689.802704 | 4 Phase Actuated Ground Mounted Traffic Controller and Cabinet (Furnished) | EA |
| C689.802708 | 8 Phase Actuated Ground Mounted Traffic Controller and Cabinet (Furnished) | EA |