DESCRIPTION

Under this item, the contractor shall install furnished steel span poles as shown on the plans and/or as ordered by the engineer.

MATERIALS AND METHOD

The poles and all component parts shall be of steel construction and shall be approved standard poles in accordance with the NYSDOT Standard Specifications, latest revision.

Cover casting or leaf covers shall be attached to the poles to conceal the anchor rods and nuts.

Poles shall have a Simplex Fitting (two bolt type) positioned as shown on the plans or as directed by the engineer.

BASIS OF PAYMENT

The quantity to be paid for under this item will be the number of poles placed in accordance with the plans and specifications and as directed by the engineer.

The price bid for these items shall include all work necessary to complete the installation.

Payment will be made under:

| Item No. | Item | Pay Unit |
| --- | --- | --- |
| C689.9942 | Steel Span Pole - Anchor Bolt Base (Furnished) | EA |