DESCRIPTION

The work shall consist of furnishing and installing working navigation lights at the locations indicated on the Contract Plans.

MATERIALS

Navigation lights and appurtenances shall generally conform to the details shown on the Contract Plans. In addition, all navigation lights shall:

a.)	Be watertight and have watertight appurtenances

b.)	Be weatherproof and have weatherproof appurtenances

c.)	Meet the minimum U.S. Coast Guard Requirements for visibility

d.)	Be vandal resistant

e.)	Be capable of being maintained from the top surface of the superstructure

f.)	Have a lamp capacity of 8,000 hours minimum. (This requirement may be met by automatic rotating lamps.)

g.)	Be capable of being locked firmly in the normal operating position.

h.)	Be installed by means of steel corrosion-resistant, vibration-resistant bolts and fasteners.

i.)	Be so designed that maintenance personnel, during their normal course of duties, will not be exposed to electrically live parts.

Conduit, couplings, and bends shall be 2” diameter hot-dipped galvanized rigid steel pipe conforming to NYSDOT Standard Specifications, Material Specification 723-20, Metal Steel Conduit, Zinc Coated, latest revision.

Wire shall be as shown on the Plans. The minimum size of conductors shall be no. 10 as designated by Underwriter's Laboratory Specifications for single-conducting.

Riser assembly shall conform to the requirements of NYSDOT Standard Specifications Subsection 723-20, latest revision.

The lens shield mounting hardware shall conform to the requirements of NYSDOT Standard Specifications, Section 715-Castings, Forgings, and Metals, latest revision, and be corrosion resistant coated as required in NYSDOT Standard Specifications, Section 719-Metal Coatings, latest revision. The lens shield shall be constructed of a polycarbonate bullet resistant sheeting with a minimum thickness of 1/8”.

Expansion Bolt Anchors shall conform to the requirements of NYSDOT Standard Specifications, subsection 567-2.01A5, latest revision.

Photocontrol heads shall conform to specifications shown on the Contract Plans.

Hanger plates, angles, studs, bolts and miscellaneous hardware shown on the Plans shall conform to the requirements of NYSDOT Standard Specifications subsection 715-01, Structural Steel, latest revision and hot-dipped galvanized by NYSDOT Standard Specifications subsection 719-01, Galvanized Metal Coatings And Repair Methods, latest revision.

A service switch shall be furnished and placed in a lighting junction box as indicated on the Plans, or as ordered by the engineer. The service switch shall  be 30 ampere, 2 pole, solid neutral, fused device in a weatherproof enclosure. It shall be attached to a side wall of the junction box above the floor of the box in a manner satisfactory to the engineer.

All electrical equipment shall conform to the NEMA Standards and be UL approved. All material and workmanship shall conform to the latest requirements of the "National Electrical Code"; the rules of the New York State Public Service Commission; the standards of the ASTM; the ASA; local power company rules and any local ordinances which may apply. Differences in standards or code requirements shall be resolved by the engineer.

Navigation lights and appurtenances may be supplied by any one of the following manufacturers, or an equal approved by the engineer.

Pennwalt Corporation

Automatic Power Division

Houston, Texas

Crouse-Hinds Company

Syracuse, New York

Guest Corporation

Bloomfield, Connecticut

Tideland Signal Corporation

Houston, Texas

Federal Sign and Signal Corporation

Chicago, Illinois

B & B Electromatic Corporation

Norwood, Louisiana

Wallace & Tiernan, Inc.

Bellville, New Jersey

Shop drawings will be required. They shall meet the applicable requirements of the New York State Steel Construction Manual, except that they shall be delivered to the MCDOT for approval.

Navigation lights and appurtenances will be accepted by the engineer, at the work site, upon written certification, by the contractor, that all the requirements of this specification have been met.

CONSTRUCTION DETAILS

Navigation lights and appurtenances shall be stored in a manner which will prevent damage. They shall be stored in a place acceptable to the engineer until such time as they are actually installed.

Immediately prior to installation, navigation lights and appurtenances shall be inspected for damage by the engineer. All material which the engineer determines is damaged or otherwise unusable, shall be repaired by the contractor, or replaced in kind by the contractor. The engineer shall make the final determination as to whether damaged material shall be repaired or replaced. Material which the engineer has determined is not usable shall be removed from the work site by the contractor.

Navigation lights shall be installed in the manner indicated on the Contract Plans. Location and lantern color shall be in accordance with U.S. Coast Guard requirements shall rule.

The lens shield shall be constructed in such a manner so as to conform to the general configuration of the lamp lens it is protecting. The lens shield and associated mounting hardware shall be constructed in such a manner that they will in no way diminish the U.S. Coast Guard minimum standards for visibility of navigation lighting.

The contractor shall install 180 degree lens shields on all red navigation lights and 360 degree lens shields on all green lights.

Photocontrol heads shall be installed as indicated on the Plans.

Navigation lights shall be in working order upon completion of installation.

METHOD OF MEASUREMENT

Payment will be made at the lump sum price bid.

BASIS OF PAYMENT

The lump sum price bid shall include all labor, equipment and materials necessary to complete the work except that conduit, pullbox, and cast iron junction boxes will be paid for under their respective items.

Progress payments will be made. Forty percent of the unit price bid will be paid for upon delivery, acceptance and proper storage of the navigation lights and appurtenances.

The remainder of the unit bid price will be paid upon complete installation of the navigation lights, in working order.

No additional payment will be made for any repair work or replacement of materials when the work is done due to the engineer's determination that material is unusable.

Payment will be made under:

| Item No. | Item | Pay Unit |
| --- | --- | --- |
| C665.99 | Navigation Lights | LS |