DESCRIPTION

This work shall consist of furnishing and installing Sign Post Sleeves as shown on the MCDOT standard detail  and to the satisfaction of the engineer.

MATERIAL

The sleeve shall be 3’-0” x 3 ½”  I.D. pipe, galvanized and standard weight.  Concrete shall be Class A concrete in accordance with NYSDOT Standard Specifications, Section 555, latest revision.

METHOD OF MEASUREMENT

The quantity paid for will be the number of sign post sleeves installed in accordance with the Contract Documents or directed by the engineer.

BASIS OF PAYMENT

The unit bid price for each sign post sleeve shall include the cost of pipe, concrete and other materials, labor and equipment necessary to complete the work to the satisfaction of the

Engineer.

Payment will be made under:

| Item No. | Item | Pay Unit |
| --- | --- | --- |
| C686.05 | Sign Sleeve | EA |