BMP Summary Sheet

Department Name:

Category of Municipal Operations:    Street and Bridge Maintenance

BMP Title: Graffiti Removal

BMP Description: Graffiti removal activities are to be scheduled during dry weather. When graffiti is removed by painting over, implement the procedures under Painting and Paint Removal. Nearby storm inlets are to be protected prior to removing graffiti. Runoff from sand blasting and high pressure washing should be directed into a landscaped or dirt area. If such an area is not available filter runoff through an appropriate filtering device (e.g. filter fabric) to keep sand, particles and debris out of storm sewers. When power washing using cleaning compounds, nearby storm inlets are to be plugged and water is to be vacuumed/pumped to the sanitary sewer. Waterless and nontoxic chemical cleaning methods (e.g. gels or spray compounds) should be used when possible.

Measurable Goals:

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Category of Municipal Operations:    Street and Bridge Maintenance

BMP Title: Paint and Paint Removal

BMP Description: Paint and materials are to be transported to and from job sites in containers with secure lids and tied down to the vehicle. Do not transfer or load paint near storm drain inlets or waterways. Spray equipment is to be tested and inspected prior to starting to paint. Tighten all hoses and connections and do not overfill paint container. Nearby storm drain inlets are to be plugged prior to starting painting in areas where there is a significant risk of a spill reaching the drain. Remove plugs when the job is complete. Storm drain inlets are to be covered prior to sand blasting. If a bridge crosses a waterway work should be performed on a maintenance traveler, platform or over suspended netting or tarps to capture paint, rust, paint removing agents or other materials to prevent discharge of materials to surface waters. If sanding, use a sander with a vacuum filter bag. Capture all cleanup water and dispose of properly. Unused paint will be taken to the Monroe County Household Hazardous Waste Facility.

Measurable Goals: Staff retraining or continuing education activities related to policies and procedures

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Category of Municipal Operations:    Street and Bridge Maintenance

BMP Title: Bridge Repair Work

BMP Description: Prevent concrete, steel, wood, metal parts, tools and other work materials from entering storm drains or waterbodies. Thoroughly clean up the job site when repair work is completed. If surface cleaning, painting and paint removal, and graffiti removal are performed implement the appropriate procedures as outlined in those BMPs.

Measurable Goals: Number of bridge repair/replacement projects with incorporated pollution prevention or streambank erosion control components Erosion control and drainage measures implemented for roads.

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Category of Municipal Operations:    Street and Bridge Maintenance

BMP Title: Unpaved Roads and Trails

BMP Description: Stabilize exposed soil areas to prevent soil from eroding during rain events. This is particularly important on steep slopes. Roadside areas with exposed soils should be vegetated with a mulch or binder that will hold the soils in place while the vegetation is establishing. Native vegetation should be used if possible. If vegetation cannot be established immediately, apply temporary erosion control mats/blankets, straw or gravel as appropriate. In roadside areas where sediment is already eroded and mobilized temporary controls should be installed. These may include: silt fences, fabric dikes, hay bales staked in place, or any other appropriate measure.

Measurable Goals:

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Category of Municipal Operations:    Street and Bridge Maintenance

BMP Title: Roadway Patching, Resurfacing and Surface Sealing

BMP Description: Patching, resurfacing and sealing are to be scheduled for dry weather. Material stockpiles are to be kept away from streets, gutter areas, storm drain inlets or waterways. Piles are to be bermed or covered during wet weather to prevent runoff. Preheating, transfer or loading of hot bituminous material is to be done away from drainage systems or waterways. Where applicable, nearby storm drains are to be covered before applying seal coat, slurry seal etc. Covers are to be left in place until job is complete and until all water from emulsified oil sealants has drained or evaporated. Clean any debris from storm drain inlets when the job is complete. Excess material is to be prevented from entering streets or storm inlets. There shall be a designated area for cleanup and proper disposal of excess material. To avoid runoff, only as much water as is necessary will be used for dust control. Waterways

Measurable Goals:

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Category of Municipal Operations:    Street and Bridge Maintenance

BMP Title: Street Sweeping and Cleaning

BMP Description: A consistent sweeping schedule is to be maintained. Street cleaning is only to be performed during dry weather if possible. Wet cleaning or flushing of the street is to be avoided where possible. When possible, sweeping frequency will be increased based on factors such as traffic volume, land use, field observations of sediment and trash accumulation, proximity to water course. Sweepers are to be operated at manufacturer requested optimal speed level to increase effectiveness. Vacuum or regenerative air sweepers will be used in the high sediment and trash areas. Accurate logs of the number of curb-miles swept and the amount of waste collected are to be kept. Dispose of sweeping debris and dirt at a landfill. Do not store swept material along the side of the street or near a storm drain inlet. Debris storage is to be kept to a minimum during the wet season. Piles will be contained by a berm or covered. field

Measurable Goals: Approximate quantity (tons or cubic yards) of debris cleaned from streets, sidewalks and parking lots. Staff retraining or continuing education activities related to policies & procedures

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail: