BMP Summary Sheet

Department Name:

Category of Municipal Operations:      Vehicle and Fleet Maintenance

BMP Title: Vehicle and Equipment Cleaning

BMP Description: Mark the area clearly as a wash area, which should be covered or bermed to collect wash water and direct it to a treatment or disposal facility. Use biodegradable, phosphate-free detergents for washing vehicles as appropriate. Design wash areas to properly collect and dispose of wash water when engine cleaning is conducted and when chemical additives, solvents, or degreasers are used. Consider washing vehicles and equipment inside the building if washing must occur on-site. If washing must occur outside, use designated paved wash areas. If a paved area is not available for outdoor washing, it should be done over a gravel or grassed area with cold water and no soap. Cover the wash area when not in use to prevent contact with rain water. Consider filtering and recycling wash water. Discharge all wash water to a sanitary sewer, holding tank, or a process treatment system after consulting with the local sewer authority to find out if pretreatment is required.

Measurable Goals: Create and mark the wash area in your facility. Report number of facilities where proper disposal of wastewater has been implemented. Train fleet maintenance staff on policies, procedures, BMPs and stormwater management.

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Category of Municipal Operations: Vehicle and Fleet Maintenance

BMP Title: Vehicle and Equipment Fueling

BMP Description: Spot clean leaks and drips routinely. Leaks are not cleaned up until the absorbent is picked up and disposed of properly. Label drains within the facility boundary to indicate whether they flow to an oil/water separator, directly to a sewer, or to a storm drain. Post signs to remind employees not to top off the fuel tank when filling and ban employees from changing engine fluids at the same location. Report leaking vehicles to fleet maintenance. Equip catch basins with chambers to remove large particles from stormwater in impervious areas. Also maintain these devices. Release accumulated non-contaminated stormwater prior to next storm. Install overflow protection devices on tank systems to warn operator to shutdown transfer pumps when the tank is full. Install protective guards around tanks and pipes to prevent damage. Clearly tag or label all valves. Maintain clean fuel-dispensing areas using dry cleanup methods. Use secondary containment when transferring fuel from the truck to the fuel tank, and cover nearby storm drains. Design fueling areas to prevent stormwater runoff and spills, such as covering the area with a roof structure, paving the area with concrete rather than asphalt and fitting fuel nozzles with hold automatic shutoffs. Apply a suitable sealant that protects the asphalt from spilled fuels in areas where covering is not feasible.

Measurable Goals: Clearly label all drains and valves in the facility for employees to know where the water is ending up.

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail:

BMP Summary Sheet

Department Name:

Category of Municipal Operations:     Vehicle and Fleet Maintenance

BMP Title: Vehicle and Equipment Repair

BMP Description: Whenever feasible, move maintenance and repair activities indoors. Store idle equipment containing fluids under cover. Avoid hosing down work areas, but if work areas are washed, collect the water and direct to sanitary sewer. Post signs to indicate storm drains and sinks are not to receive hazardous wastes. Designate a special area, with no connections to the storm drain, to drain motor fluids. Collect leaking or dripping fluids in drip pans or containers, and drain all fluids immediately. Promptly transfer used fluids to proper waste or recycling drums. If equipment is to be stored outside, all fluids should be drained first. Keep equipment clean, don’t allow excess grease and oil buildup. If temporary work is being done outside, use a tarp, ground cloth, or drip pans to capture all spills and drips, and dispose of properly. Regularly inspect vehicles and equipment for leaks and repair immediately.

Measurable Goals: Number of cleanouts of oil and grit separators or similar maintenance operations for site draingage structures Recycling program results for oil, antifreeze, other fluids

Timeline/Implementation Schedule:

Specific Components and Notes:

Responsible Party for this BMP Indicate who specifically is responsible for the implementation and monitoring of this BMP. This should be the individual who is actively involved with the BMP. Name: Department: Phone: E-mail: